## Rain Scavenging of Tritiated Water Vapour: A Numerical Eulerian

Stationary Model

D. Atanassov a  *, D. Galeriu b

a National  Institute  of  Meteorology  and  Hydrology, Department “Content  of  the atmosphere and hydrosphere “,  66 Tzarigradsko Chaussee, 1784 Sofia,  Bulgaria, Dimiter.Atanassov@meteo.bg

b “Horia Hulubei” national Institute for Physics and Nuclear Engineering, Department of Environmental Physics and Life, 407 Atomistilor St., POB MG-6, Bucharest – Magurele, RO-077125, Romania

* Corresponding author:  National  Institute  of  Meteorology  and  Hydrology , 66 Tzarigradsko Chaussee, 1784 Sofia,  Bulgaria,

email: Dimiter.Atanassov@meteo.bg,  tel.: (+359 2) 4624582, fax: (+359 2)  9880380

Abstract

Tradition in tritium washout modeling is to unite the washout model with a Gaussian plume model describing dispersion of tritium vapor in the atmosphere. In the present study, an alternative approach to modeling the washout process is proposed. A numerical Eulerian model that describes washout independently of dispersion is developed. The model is to be used as a subroutine in tritium specific models interfaced with any sophisticated dispersion model.

Different size distributions of raindrops and different formulae for drop downfall velocity are considered.  A sensitivity analysis to these and other model parameters is performed. Recommendations for some numerical techniques are made. The sensitivity analysis has shown that the washout process is influenced most significantly by rainfall parameters and air temperature: different raindrop size distributions cause differences of up to about 70 % in the washout outputs; a change of 150C in the air temperature causes an effect of about 50 %. Unlike temperature, which is usually well known, rainfall parameters are difficult to establish precisely, that can lead to substantially wrong washout estimates.

Results are presented showing calculated values of tritium concentrations in rain, tritium downward flux, and washout coefficients for different tritium vapor profiles, rainfall rates and air temperatures. The general conclusion is that the washout process is too complex to be described comprehensively by the simple washout coefficient concept. The approach proposed here for directly calculating the outputs like concentration and flux is preferable; anyway the washout coefficient is needed mostly for the assessment of these outputs. The biggest potential for improvements in tritium washout modeling is related to comprehensive input information for cloud and rain processes that becomes easily available today.

Keywords:  washout, scavenging, tritium, tritiated water (HTO) vapor

1.  Introduction

The theory of washout of gaseous pollutants from the atmosphere was first comprehensively applied to tritiated water (HTO) vapour by Hales (1972 a, b) and his HTO washout concept has not changed substantially up to now.  The present study will closely follow the established approach, concerning the individual raindrop problem.  What is known about this topic will be reviewed in Section 2, and the assumptions used here will be indicated.

There are two peculiarities of the traditional approach to washout modeling that will be challenged here: 1) Following Hales (1972 a, b), all authors combine the washout model with Gaussian plume dispersion model, which allows analytic expressions for the washout output characteristics to be obtained; 2) The traditional goal of HTO washout studies is to determine characteristics like washout ratio and washout coefficient.  Once these have been determined, they are applied as coefficients in simple expressions in more general models to determine the absolute washout outputs like HTO downward flux and concentration in rainfall.  The problem with this approach is that these coefficients account the shortcomings of the Gaussian models. In addition, if the coefficients are to be determined accurately, they  have to be considered as functions of height of the HTO source, distance from the source, atmospheric stability, air temperature, etc. (Belot, 1998), which is a difficult task in real situations.  More recently the wet deposition of pollutant was expanded for five kinds of Gaussian plume formulations (Hales, 2002).

IFIN-HH was selected to implement the European Community project RODOS in Romania and to develop a tritium module – FDMH (Food Dose Module Tritium) (Galeriu et al., 2000).  Starting with an older revision of the topic (Ogram et al., 1992) an update on dry and wet deposition was done (Melintescu, 2002) and the need of improvement wet deposition modeling was noted.  This paper is the first in our attempt for such a goal.

A new, numerical Eulerian approach, free from the above shortcomings, will be proposed in Section 3 of this paper.  The washout model will be formulated separately, independently of any dispersion model.  Thus it can be coupled to any simple or advanced dispersion model.  The proposed model will calculate absolute outputs directly, thus making washout ratio and washout coefficient unnecessary.  A sensitivity analysis will also be done (Section 4) and some typical results will be presented and discussed (Section 5).

2.  HTO condensation at a microphysical level

2.1 Formulation of the individual drop problem

It is convenient to consider the condensation of gaseous pollutant to a raindrop as a consequence of a two step process: first, the gaseous pollutant is transferred to the drop’s surface by convection and diffusion through the air (gas-phase step); second, the dissolved pollutant is dispersed within the drop (liquid-phase step). One of the most significant features of Hales’ works (Hales, 1972 a, b) is the combination of the two steps by introducing an “overall” mass-transfer coefficient .  The advantages are that the problem becomes a one-step problem and that the difficulty in determining the interfacial pollutant concentrations at the drop-air interface is overcome.  The disadvantage is in defining the overall mass-transfer coefficient .

The basic equation (7) in (Hales, 1972a) and equation (1) in (Dana et al., 1978)) describing the condensation of gaseous pollutant into a raindrop is written in terms of mole fractions.  Using Henry’s law (IUPAC 1993), after some  transformations, the equation can be rewritten in terms of concentrations (Ogram, 1985):

=  ,	 				         (1)

where:

- the concentration of the liquid phase HTO in the drop (g.cm-3);

- the time (s);

- the concentration of the vapor phase HTO in the drop's environment (g.cm-3);

- the drop's diameter (cm);

- the mentioned above overall mass-transfer coefficient (cm.s-1);

- a dimensionless coefficient given by:

=  , 					         (2)

where:

- temperature (ºK);

- Henry’s law constant (atm; 1atm = 1013.25 hPa = 1.01325. 105 N.m-2);

-  density of the water (=1 g.cm-3);

- universal gas constant ( = 82.05 atm.cm3.K-1.moles-1);

- molecular weight of water (=18 g.mole-1).

The Henry’s law constant  depends only on , and following Hales (1972a) and Ogram (1985), its values used here for the case of tritium are based on the data of Jones (1968) and Van Hook (1968).

The transport of liquid HTO within the drop is due to: 1) circulation of the water inside (convection); 2) molecular diffusion.  For a drop falling in the real atmosphere, the friction with the air causes an intensive convection motion inside the drop.  The liquid HTO is mixed up so rapidly by the convection that molecular diffusion can be neglected.  Then, the overall mass-transfer coefficient  is defined by the following semi-empirical expression, referred to as the Froessling equation (Hales, 2002):

=     =   ,   	 	        (3)

where:

- Reynolds number;

- Schmidt number;

- gas phase diffusion coefficient of HTO (cm2.s-1);

- drop's downfall velocity (cm.s-1);

-  kinematic viscosity of the air  (cm2.s-1).

Only this case, known as gas-phase limiting, will be considered here because the stagnant drop case (in which there is no convection and molecular diffusion is the sole mechanism for transport into the drop), is unlikely in the real atmosphere and is not considered in the HTO washout literature except by Hales (1972 a, b) and his coworkers (Dana et al., 1978).

In some studies,  and  are assumed to be constants.  Following Ogram (1985), they will be considered here as a function of temperature  and atmospheric pressure:

=  					         (4)

= ,					         (5)

where:

- temperature (ºK);

- atmospheric pressure (hPa).

Two classical formulae for the drop downfall velocity will be used. The first one is suggested by Best (1950):

=  ,			             	        (6)

where:

, ,   for drop diameter < 0.015 cm

, ,   for drop diameter > 0.015 cm.

The other formula considered here is according to Kessler (1969):

=   .			             	        (7)

2.2   Solution of the individual drop problem

The solution of equation (1), if , , and  are constant in time is:

= + 	,			         (8)

where = is the concentration at the initial moment  .

The HTO drop’s concentration  tends to the equilibrium value.  The quantity    is a characteristic time for the rate that  changes.  Depending on the values of  and , the concentration  could increase when <(condensation) or decrease when >(evaporation).

If some of the parameters (i.e.,,  or ) are not constant in time, the differential equation (1) may be solved numerically.  Another way to treat the non-stationary case is to apply the analytical solution (8) for short time intervals during which ,,, and  remain approximately constant.

Figure 1 shows the solutions of the non-dimensional version of equation (8) for different raindrops diameters and air temperatures:

= 							         (9)

using the following notations:

,    == 0  .

In the non-dimensional case, the equilibrium concentration is equal to 1.  In Figure 1 is presented the solution  for the first 350 s, for =850 hPa.  The smaller drops at higher temperatures reach the equilibrium state with the outside HTO vapor much faster then the bigger drops at lower temperatures. In the case = 0.9 cm, = 00C, the equilibrium concentration value of 1 is reached at more then 10 000 s (outside the Figure 1, to the far right).  The short vertical lines crossing the   lines mark the time needed for a drop with the corresponding diameter to pass through a 100 m vertical layer, according to the drop’s downfall velocity formula of Best (1950) (equation (6)).  The sensitivity of  to typical pressure changes in the atmosphere is negligible.

The drop’s diameter influences the washout process as following: 1) through the condensation, that has been discussed just above and, 2) through the drop's downfall velocity, which determines the length of time it takes the drop to pass through the HTO layer.  According to the drop's downfall velocity formula of Best (equation (6)), the time it takes a drop with diameter 0.02 cm to pass through a 100 m vertical layer is 136 s; for a drop with diameter 0.4 cm, it takes 61 s, and for a drop with diameter 0.9 cm, it takes 11 s (see the short vertical lines crossing the corresponding  lines in Figure 1).  The end result is that almost nothing condenses in the largest drops during the time when the smallest drops are reaching the equilibrium concentration.  This is a result of the combined influence of the drop’s diameter on the condensation and on the downfall velocity.

2.3 Drop size distribution (DSD)

The following empirical formulae for the drop size distribution (DSD) in the rainfall are used in the present study:

=0.08   -  DSD of Marshall-Palmer (MP), after Ogram (1985)                  (10)

=0.07  -  DSD of Sekhorn-Srivastava (SS), after Ogram(1985),    (11)

where:

- the rainfall rate (mm.h-1;  = 36 000 ml.cm-2.s-1);

- the number of drops per unit volume of air per unit increment in drop diameter around a

value .

According to the empirical Best’s formula for DSD (Best, 1950), it has:

=   					                   (12)

= - DSD of Best  (B), after Belot (1998) ,

where:

- total volumetric water contained in air (= );

= cm.

The denominator   is the volume of an individual spherical drop with diameter.

Assuming the drops are spherical, the spectral volumetric water content in the air,  (cm3.cm-3.cm-1) = (ml.cm-3.cm-1) and the total water content,  (cm3.cm-3) = (ml.cm-3), by definition are:

= 					                 (13a)

=  = .				                (13b)

The spectral volumetric water flux  (cm3.cm-2.s-1.cm-1) = (ml.cm-2.s-1.cm-1), and the total over the spectrum water flux (cm3.cm-2.s-1) = (ml.cm-2.s-1), could be calculated in the following way:

= ()       	 			  	       (14a)

= = .				                 (14b)

The total rainfall rate  appears in the calculations as an argument through the empirical equations (10) - (12). In the model's applications,  will be taken from the observations.  When it is necessary to clarify this, the rainfall rate will be denoted as  - "measured" total rainfall rate.  Because the formulae for  and  are, in principle, non-coherent empirical formulae, the value  resulting from the integral (equation (14b)) may not equal the value of  appearing as an argument in . In this way, the spectral water content of the air  and the spectral rainfall rate , calculated from equations (13a) and (14a), noted below as  and, do not correspond to measurements, in the sense that the integral of spectral rainfall rate over the spectrum, i.e. the integral (equation (14b)) does not equal the measured value.  The values  and , normalized to the measurements are:

() = ()+ ()			                   (15)

() = 	.			                   (16)

Now, if  and  are set in the integral (equation (14b)), the calculated value  will equal the value of.  In fact, equations (15) and (16) represent normalization to the input data.  The effect of the normalization is discussed below in Section 4.1.

3.  Modeling of HTO washout from the atmosphere

3.1   Formulation of the model

In the studies dedicated to HTO washout, the only required information for the rain event is the rainfall rate.  The following commonly accepted assumptions compensate for unknown or unused data:

- raindrops are spherical and their size remains constant during the downfall;

- drops fall vertically with a constant velocity;

- there exists a height, , usually assumed to be the cloud's bottom, that is the level from

which all raindrops start to fall;

- the raindrop spectrum is known (from equations (10), (11) or (12)), and does not change with

height;

- the processes are stationary: the rain spectral characteristics, the geometry of the rain cloud, the

geometry of the HTO cloud do not change during the time when the smallest raindrops are falling

from   to the ground surface.

Satisfaction of most of these assumptions is not likely.  Real processes are much more complex then the idealized picture described above.  Nevertheless, these assumptions will be used here, because, to account for more complexity, detailed data of cloud and rain phenomenon must be obtained, and the goal of the present study is to improve other aspects of existing HTO washout knowledge.

HTO washout models are developed as 1-dimensional vertical models taking advantage of the assumption that raindrops fall vertically.  In addition to the data for the rain event, the present model needs the profiles of atmospheric pressure and temperature and the profile () of the HTO vapor.  In traditional HTO washout studies that use a Gaussian dispersion model, the input () profile is replaced by input data such as the HTO source, its height, emission rate, distance from it, and atmospheric stratification.

A contemporary HTO atmospheric transport modelling system should consist of at least the following models: a model describing the dispersion of HTO vapor in the atmosphere, dry deposition and wet deposition (washout) models, and a meteorological preprocessor, ensuring the necessary meteorological input for the mentioned models.  The washout model presented here is constructed as a subroutine of such a transport modelling system.  The washout model takes the () profile from the dispersion model, calculates the washout, and returns the () profile, corrected by the HTO scavenged by the rainfall.  This exchange between the dispersion and the washout models takes place at each time step, over each horizontal grid cell (point).

3.2 HTO washout calculations - numerical scheme

A vertical grid with a step  is introduced below cloud level, .  It is assumed that the liquid HTO in the raindrops at that level () is in equilibrium with the surrounding HTO vapor ().  Equation (1) is applied to layer by layer downward below, for each drop size interval.  All the parameters presented in equation (1) are assumed constant within a grid layer. This makes it possible to apply the analytic solution (equation (8)) to a drop for the time necessary to pass through the grid layer. Before applying equation (8) to a drop with diameter  in layer, its passing time  is determined, according to the accepted formula for the drop’s downfall velocity (see Section 2.1).  The concentration, calculated for this drop, after it has spent time  in the -th layer, is used as initial condition for the next -st layer.  The calculations for the last 1-st layer, the layer above the ground, give the spectral mass concentration of liquid HTO in raindrops  at the ground surface.

3.3 HTO washout output characteristics

The spectral mass concentration of liquid HTO in the air, and the corresponding total spectrum concentration in air, i.e. the mass of liquid HTO in unit space volume are:

=() ()					                 (17a)

=,	(g.cm-3)  .				                 (17b)

The total mass of liquid HTO dissolved in the unit volume of liquid water in air, i.e. the total mass concentration of liquid HTO in the water in the air, is

=  =  ,	  (g.cm-3)  = (g.ml-1) .	    	  	       (18)

The spectral and total mass of liquid HTO passing through unit surface area perpendicular to  per unit time, i.e. spectral and total mass flux of liquid HTO, are correspondingly:

== ()()() ,	( g.cm-2.s-1.cm-1)      		       (19a)

=,  (g.cm-2.s-1) 	.			                   (19b)

If the flux  of liquid HTO at the ground surface is divided by the rainfall rate, the result is the mass concentration of the liquid HTO in the falling rain water:

=  =    ,	(g.cm-3) = (g.ml-1)  .      	       (20)

Both quantities  (equation (18)) and  (equation (20)) refer to the total mass of liquid HTO per unit volume of liquid water.  The difference is that in equation (18) the water is in the air, while in equation (20), the water is passing through some surface, in particular, the soil surface.

The traditional goal of HTO washout studies is to determine the washout ratio:

=   					                   (21)

and the washout coefficient :

=  ,   (s-1)  .				                   (22)

where - the amount of HTO in a column with a bottom of unit area (g.cm-2).

Two types of outputs can be distinguished: absolute or relative characteristics.  The absolute outputs include liquid HTO concentration in the air (equation (18)) or in the rainfall (equation (20)), as well as the downward flux of liquid HTO (equation (19)).  The relative outputs are the washout ratio (equation (21)) and washout coefficient (equation (22)).  The last two are characteristics of the washout process that are needed to calculate the absolute outputs.  Because the present model is designed to calculate the absolute outputs directly, the washout coefficient will be considered below only in order to discuss this concept.

4. Sensitivity analysis

The values of the model’s outputs depend on a list of inputs: , , , …  There are inputs of different type, some of them are numbers – vertical grid step, minimum raindrop size dRmin; others are formulae - downfall velocity (equation (6) or (7)), drop size distribution ( (10), (11) or (12)); others are vertical profiles – air temperature, atmospheric pressure and HTO vapor.  An overview of the inputs and their variability is presented in Table 1.  The model is able to treat varying with  air temperature and atmospheric pressure, but in the examples below they are considered as constant with, i.e  and  are considered as numbers, not as profiles.  The sensitivity of the model’s outputs to its inputs will be investigated using the typical variability of the inputs given in Table 1.

The present study is restricted to a local sensitivity analysis, varying one input  at a time, for fixed others inputs ,,,…  If  and  are two values of the model output , obtained by two model runs, both for same inputs ,,,…, but the first one for , and the second one for ,  the quantity:

= 100% 	                   (23)

will be used below as an assessment criterion for the local sensitivity of  to .   The calculation of  will be performed many times for the same and , for different , , ,… taken in their range of variability (see Table 1).

The HTO concentration in the falling rain, the flux of falling liquid HTO  and the washout coefficient  are related to each other.  It is easy to prove, that the criterion  will have the same value for and for, if the rainfall rate  has one and the same value in the two model runs to determine; similarly,   will have the same value for and for, if the amount of HTO in a vertical column  has one and the same value in the two model runs.  Because in the runs to determine S, the values of  and  will not be changed, the sensitivity of , and  to  will be established at once.  The sensitivity of the mass concentration of liquid HTO in water in the air  should be considered separately.

A simple Gaussian plume dispersion model will be used only in order to generate  profiles at 10 distances from the source, from 100 m to 33 000 m.  It is assumed that the source is at 60 m height, the emission rate is 1 000 g.s-1, the wind speed is 10 m.s-1 and the atmospheric stability is neutral.  The sensitivity to the distance from the source could be considered as sensitivity to the profile and magnitude of the HTO vapor: close to the source, the vertical gradient of  is significant, while far away from the source,  tends to a constant of small magnitude.  The maximum value of the assessment  for all the 10 distances will be presented in the following considerations, unless otherwise noted.

4.1 Sensitivity to the numerical parameters

The drop diameter  is present in the denominator of some formulae.  Because a negligible part of the rainfall is contributed by drops smaller than some size, it is necessary and meaningful to establish some minimum drop size dRmin, below which numerical calculations will not be performed.  To determine the sensitivity of the model's outputs to dRmin, a series of runs was performed for = dRmin = 0.02 cm and = dRmin = 0.000005 cm.  The biggest value of  (see equation (23)) found was 0.6 % for= and 0.2 % for =,,  in the case of =0.5 mm.h-1,  according to Kessler (1969) and DSD of MP.   A second series of runs was performed for = dRmin = 0.1 cm and = dRmin = 0.02 cm.   The biggest value of  found was 97.6 % for =, in the case of =0.5 mm.h-1, according to Best (1950) and DSD of MP and 8.9 % for =,, , in the case of =30.0 mm.h-1,  according to Best (1950) and DSD of B.   All calculations were performed for an air temperature of 150C constant throughout; these values of  are the maximum ones with respect to the distance from the source.  Obviously, the neglect of drops with diameter less than 0.02 cm will not lead to significant errors, and the value of dRmin =0.02 cm is a good choice for a lower limit of the integration.  The maximum drop size is determined by the rainfall rate  and by the accepted DSD formula.

The sensitivity of the model’s outputs to the vertical grid step  depends on the input profiles.  The mechanism of the dependence can be easily understood because the small scale features of the profiles cannot be taken into account from a grid with large step .  An increase of  from 2 m to 10 m changes the values of ,, and  by -18 % from their values when = 2 m; the value of  is changed by about 3 %.  An increase of  from 2 m to 20 m changes the values of, , and  by -86 %; the value of   is changed by about 9 %.   Different sensitivities of  and  to  are explained by the presence of  in the denominator of equation (22).    As  is also calculated numerically, its value depends on : it equals to 0.4101x10-3 g.cm-2  for =10 m and to 0.4989x10-3 g.cm-2 for =2 m.   The smaller sensitivity of  is not a real advantage, because in applications,  will be used to determine the absolute outputs and the errors corresponding to the absolute outputs will appear.  The results above are obtained at a distance of 100 m downwind of a source; for   =150C.  Away from the source, where the gradients of HTO vapor profile  are smaller, the sensitivity to the grid resolution is smaller: at a distance of 400 m downwind, the above values become less than 1 %.  The influence of   and on the sensitivity of the outputs to  is less significant than the influence of .  The influence of the cloud-rain parameters on the sensitivity to  is also insignificant, because in all washout modes, including the present one, the cloud-rain parameters are assumed to be constant throughout .  Within an accuracy of 1 %, the sensitivity to  is the same for all DSD, for all rainfall rates and for all downfall velocities in Table 1.

The step =10 m can be considered acceptable for many purposes, but the step =20 m will often be unacceptable.  These assessments concerning could be considered as requirements to the vertical resolution of the input profiles of the washout model.

The normalization procedure (equations (15), (16)) does not affect, because the effect on  and  is compensated.  By definition the relative effect 100 %(-)/ on  and on  is quantitatively equal.  Its value, averaged over the distance from the source, varied between 6 % in the case of =30.0 mm.h-1,  according to Kessler (1969) and DSD of MP and 62 %, in the case of =30.0 mm.h-1,  according to Best (1950) and DSD of SS.  These assessments negligibly depend (less then 0.5 %) on the HTO vapor profile.  The conclusion is that in any case (any value of , , and any choice of DSD), the normalization procedure must be applied.

4.2 Sensitivity to the atmospheric and rain input characteristics

The sensitivity to DSD and to the formula accepted for the downfall velocity  is considered for three different rainfall rates : a light one of 0.5 mm.h-1, a typical one of 3 mm.h-1 and a heavy one of 30 mm.h-1.  The dependence of the outputs on  will be discussed in Section 5.

Sensitivity of model outputs ,,,  to the DSD is presented in Table 2.  Let us denotes  the value of one of these outputs calculated with the Marshall-Palmer’s DSD (MP),  - the same calculated with Sekhorn-Srivastava’s DSD (SS), and  - the same calculated with Best’s DSD (B).  At the first row ("SS-MP") of the Table 2, the value of the criteria from equation (23) =100%(-)/ (0.5(+)) is calculated for i=2, j=1; on the second row ("B-MP") - for i=3,j=1; on the third row ("B-SS") - for i=3, j=2.  The result for , maximum by absolute value with respect to the distance to the source is presented.  The air temperature is 150C.  The value of  S  for  A = Cc varies from less than 1 % (between DSD of SS and MP, in case of R=3 mm.h-1) up to 72 % (between DSD of B and SS, in case of R=30 mm.h-1, vz according to Best (1950)).  For A = , and  the value of S varies from less than 1 % (between DSD of SS and MP, in case of R=3 mm.h-1) up to 69 % (between DSD of B and SS, in case of R=30 mm.h-1, vz according to Kessler (1969)).

The sensitivity to the drop downfall velocity formulae (equations (6) and (7)) is weaker.  The maximum value of = 100 %(-)/ (0.5(+)), for =,,,, where  is calculated by equation (7) and  by equation (6) is less then 8%.

As must be expected from the analysis of the condensation to an individual drop (Section 2.2), sensitivity to air temperature is significant.  The value of = 100%(-)/(0.5(+)) for a temperature change from 00C to 150C  is presented in Table 3.  Such a change of 150C produces an effect of up to about 60 % in  and 54 % in, ,.  The effect caused by typical variations in atmospheric pressure is less the 2 %.

Air temperature variations in time and in the vertical of the order of 150C are usual in the atmosphere, and the influence of temperature on the washout process is as significant as the influence of the rain parameters.  Unlike the rain parameters, which are difficult to establish accurately, temperature is usually well known.

5.  Analysis of some results

Some of the parameters considered in Section 4, once fixed, will be not varied, but the rainfall rate , the profile of the HTO vapor  and the air temperature  will be varied.  Variations in atmospheric pressure have only a small effect on predicted washout values.  The Marshall-Palmer’s DSD (equation (10)) and the drops' downfall velocity according to Best (1950)  (equation (6)) were used to calculate the next examples.

Six  profiles were manually determined, and the model was run with them instead of using the Gaussian dispersion model.  The value of  is constant with  in the first three “profiles”, but the magnitudes of  are very different: 1.0x10-6, 1.0x10-9 and 1.0x10-21 g.cm-3, respectively for profiles №1, 2, 3.  In the case of another three profiles, (№ 4, 5, 6), the amount of HTO in a vertical column  is identical (0.6997x10-5 g.cm-2), but their vertical distribution is quite different (Figure 2).  The model runs were performed for different rainfall rates and temperatures.

5.1 Spectral view of the washout process

Some spectral peculiarities of the washout process for the case of   profile №5 are illustrated in Figure 3.  The equilibrium concentration is bigger and the drops can accumulate more HTO when temperatures are lower (compare the equilibrium curves in Figures 3 a and b).  However, the processes of condensation and evaporation of HTO to and from the drops are more rapid at higher temperatures (Figure 1).  During the downfall of the smallest drops (0.02 cm), the HTO concentration in them follows closely the equilibrium curve at 150C but lags behind at 00C.  The HTO concentration in drops of diameter 0.075 cm reaches similar values (3.59x10-5 g.ml-1 and 4.06x10-5 g.ml-1, for 150C and 00C, respectively) near the bottom of the HTO vapor layer, but below that layer, the loss of HTO by evaporation is more rapid at 150C.  For big raindrops, the assumed layer of HTO vapor is obviously too shallow and these drops accumulate only a small fraction of the tritium they have the potential to accumulate.  A change in the thickness or the position of the HTO layer can change these results substantially.

5.2 Typical behaviour of the washout outputs

The washout outputs for the case of constant = 1.0x10-6 g cm-3 are presented on Figure 4.  The results for the two other cases of constant  scale with: larger amounts of tritium  in the atmosphere result in higher concentrations of ,  and higher flux ;  is independent on , as a direct consequence of its definition.  The interesting conclusion from these examples is that the both concentrations and  are almost independent of  (Figures 4a,b).  In contrast, and  increase linearly with increasing  on logarithmic axes (Figure 4c,d).

The washout outputs in case of the three  profiles in Figure 2 are presented in Figure 5.  Results for the HTO flux on the surface are shown with a logarithmic y axis (as well as with a linear y axis) so that the magnitude of the differences can be seen clearly.  The results for the washout coefficient  are not presented, as they are the same as the results for the flux, divided by the amount of HTO in a vertical column (= 0.6997x10-5 g.cm-2) which is identical for all cases considered in Figure 5.

Several interesting conclusions can be drawn, as following:

1) Lower temperatures result in higher concentrations of  and, and higher  (and ) (Figures 5a,b,c).  For  and, this effect is more significant for lower  than for larger  (Figure 5a,b).  For (and ), the effect is more significant for higher  than for lower  (Figure 5c - linear y-axis).

2) The dependence of  (and ) on  is similar to that in the case of constant – approximately linear increase with increasing  (logarithmic axes). In this case, however, unlike the cases of constant , the curve  has a different slope for different temperatures and for different  profiles (comparing Figure 4c with Figure 5d). Any attempt to define (or ) as a simple function of  makes it necessary to define different functions for the different temperatures and different  profiles.

3) The concentrations  and, unlike the cases of constant , depend in a complex way on , on  profiles and on air temperature.  Both concentrations  and  decrease with increasing  for temperature of 00C, by varying amounts for the different  profiles.  For conditions of 300C, and  also decrease with increasing  for profile №4, but for elevated tritium clouds (profile №5), they slightly increase with increasing . For the  profile №6 and temperature of 300C,  and  depend weakly on , similar to the case of constant , but for temperatures of 00C and 150C they decrease with increasing .

Obviously, the processes are so complex, that any changes in the thickness or height of the HTO vapor layer, or air temperature will largely influence the results.  In fact, the tritium vapor and temperature could be complex functions of z.   A change in the rainfall rate will, on the other hand, change the rain spectral characteristics.  The final effect of such changes on the washout outputs is difficult to predict without the help of a model.

The significance of the elevation and shape of the tritium cloud is obvious from Figure 6.  The concentrations and  and  are bigger when the cloud of HTO is close to the ground (profile №4), because when the cloud is high, the evaporation that occurs beneath the cloud causes a decrease in their values.  Both concentrations  and  are more sensitive to the rainfall rate when the HTO cloud is at the surface.

Figure 6d demonstrates the advantages and disadvantages of the washout coefficient concept.  If the HTO vapor is distributed homogeneously over, the value of the washout coefficient  remains the same, despite the big difference in the amount of tritium in the air  (see the  result for “profiles” №1, 2, 3 in Figure 6d).  However, if the HTO vapor is distributed unevenly throughout , even if the total amount of  is the same (profiles №4, 5, 6 in Figure 2), the values of  are different, especially for heavy rainfall rates (see the results for profiles №4, 5, 6 in Figure 6d).  Thus, if one wishes to use the washout coefficient concept, the coefficient  should be a function of the profiles, and not only a function of the rainfall rate and temperature.

6. Conclusion

This study follows the approach established by Hales (1972 a, b) concerning the processes in an individual raindrop, but some innovations concerning the washout process are made in this paper:

1) A new, numerical Eulerian modeling approach to the washout process is proposed that is independent of dispersion of HTO vapor.  The model is designed as a subroutine in models dealing with the movement of HTO in the environment.  It can be combined with any advanced dispersion model, thus avoiding the shortcomings of the Gaussian dispersion models traditionally used in HTO washout studies.  This washout model in addition, leaves the tasks of accounting for such variables such as the height of the source and the distance from it to the dispersion model.

2) The present model directly determines absolute washout outputs like HTO downward flux and concentration in rain, in contrast to the traditional approach, which considers in detail only the  relative characteristics  (the washout coefficient and washout ratio) and applies them in simple  formulae to determine the absolute washout outputs.

Different drop size distributions and downfall velocity formulae have been considered.  A sensitivity analysis to these and other parameters has been performed.  The established analysis recommends values for some numerical parameters and procedures.  A vertical grid step of 10 m is appropriate for modeling washout, especially close to an HTO source.  The calculated spectral liquid water content in the air  and the liquid water flux  has to be normalized to the measured rainfall rate.  The sensitivity analysis has also shown that both rain parameters and air temperature significantly influence the washout process.  Unlike temperature, which is usually well known, rain parameters are difficult to establish accurately, and, if incorrect, the model predictions could be substantially wrong.

Results are presented showing calculated values of the outputs (HTO concentrations in the water in the air  and in the rain water, liquid HTO downward flux  and washout coefficient ) for different HTO vapor profiles in the air , for different rainfall rates  and for different air temperatures .  The washout coefficient  can be determined as a relatively simple function of  and  (Figure 4) only in the case when  is uniform vertically.  However, if  is not uniform, the relationship between  and  becomes dependent on, i.e. on the characteristics of the HTO source and atmospheric conditions; in addition, the dependence on temperature becomes more complex (see the result for  in Figures 5c,d and Figure 6c,d).  It is not easy to define such a function even theoretically, especially when there can be more then one HTO source and temperature can change with height. Obviously, washout processes are too complex to be described comprehensively by simple concepts like the washout coefficient.  The proposed model, that directly determines,  and, accounts for the complexity possible in real situations.  The model also calculates the washout coefficient for comparative purposes, but the coefficient in the present approach has realistic different values for different sites and moments.

The present study makes some steps forward for improvement of HTO washout simulations and suggests a major cause for the large variability in the washout rate used in the past.  Appropriate experimental data for the model validation do not exist or are not available for the moment.  In addition to that, the model does not overcome some significant shortcomings remaining from traditional approach.  Most of them are related to the description of cloud-rain processes: the assumptions that the processes are stationary that the raindrops are falling down without changing their size and velocity are unrealistic.  The solution to these problems can be obtained through better input information for the cloud-rain processes.  Presently all HTO washout models, including the one presented here, use only the rainfall rate as the only input describing the rain event, despite more information can be available.  Contemporary weather radars are able to provide information about cloud and raindrops distribution in space and time, about their spectrum and movements (sometimes drops may even move upward).  A substantial reformulation of modeling approach will be necessary to incorporate this information.

Acknowledgements

We are very grateful to Phil Davis (former AECL Canada) and to Sylvie-Ring Peterson (former LLNL USA) and Anca Melintescu (IFIN Romania) for their useful comments and permanent support.  We wish to thank also, to Yves Belot (former CEA France) for his help and devotion in tritium research.  For financial support, we acknowledge to Romanian Ministry of Education and Research and Bulgarian National Science Fund of Ministry of Education and Science.

References

Abrol V., 1990, Estimation of washout of tritiated water (HTO) effluent by raindrops.  Bulletin of radiation Protection 13, 23-26.

Belot Y., 1998, Predicting the washout of tritiated water from the atmospheric plumes, Workshop of the IEA Task Group on Tritium Safety and Environmental Effect, AECL, Chalk River, Canada.

Best A.C., 1950, The size distribution of raindrops, Quart.J.Roy. Meteor. Soc. 76, 16-36.

Dana M.T., Wogman N.A. and Wolf M.A., 1978,  Rain scavenging of tritiated water (HTO). A field experiment and theoretical considerations.   Atmospheric  Environment. 12, 1523-1529.

Galeriu D., Melintesu A., Turcanu C., RaskobW., 2000,  “FDMH – The Tritium Module in RODOS – Actual Status and Perspectives”, Workshop on Tritium Behavior in the Environment, Kurri, Kumatori, Osaka, Japan,  8-9 May, 2000

Hales J. M. 1972a Scavenging of Gaseous Tritium Compounds by Rain, BNWL-1659, Battelle, Pacific Northwest Laboratories, Richland, Washington.

Hales J. M. 1972b Fundamentals of the theory of gas scavenging by rain. Atmospheric  Environment. 6, 635-659.

Hales J. M. 2002 Wet Removal of Pollutants from gaussian Plumes: basic Linear Equations and Computational Approaches.  J. Appl. Met., vol.41, 905-918

IUPAC, 1993, A Guide to IUPAC Nomenclature of Organic Compounds (Recommendations 1993), 1993, Blackwell Scientific publications, Copyright 1993 IUPAC; http://www.acdlabs.com/iupac/nomenclature

Jones, W.M., 1968, Vapour Pressures of Tritium Oxide and Deuterium Oxide. Interpretation of the Isotope Effects. , J Chem. Phys., 48, 207-214

Kessler E., 1969, On the distribution and Continuity of Water Substance in Atmospheric Circulation,  Met Monogr, vol. 10 , 32, Am Met Soc, Boston, Mass.

Melintescu A, 2002, Processes and parameters in modeling dry and wet deposition of radionuclides (in Romanian), part of PhD thesis

Ogram G.L., 1985,  Precipitation scavenging of tritiated water vapour (HTO), Report 85-233-K, Ontario hydro research division.

Ogram G.L., Bunnenberg C., and Taschner M., 1992, Key processes and Input Parameters for Environmental Tritium Models, CFFTP Report Net-Contract-No. 88-176, May 1992.

Van Hook W. A., 1968,  Vapour Pressure of Isotopic Waters and Ices, J. Phys. Chem., 72, 1234-1244

Figure1. Non-dimensional liquid HTO concentration  in drop as a function of time for different drop’s diameter (= 0.02, 0.4, 0.9 cm) and temperatures (= 0, 15, 300C).

Figure 2. Vertical profiles of HTO vapor, used as profiles N: 4,5,6  for washout calculations presented in Figures 3, 5, 6.

profile № 4                        profile № 5                       profile № 6

Figure 3. Changes of HTO concentration in drops of different diameter (0.02, 0.075, 0.25 cm) during their downfall, for the HTO profile №5 from Figure 2 and for constant over  temperatures of 150C and 00C.  Rainfall rate is 3 mm.h-1,  DSD is according to Marshall-Palmer (Ogram, 1985), downfall velocity is according to Best (1950).

Figure 4. Washout outputs for homogeneous distribution of 1.0x10-6 g cm-3 (profile №1), as a function of rainfall rate (0.5, 3.0, 30 mm.h-1), for different temperatures: 0 0C (diamond), 15 0C (circle), and 30 0C (square).

| a) HTO concentration in the water in the air | b) HTO concentration in the rain water | c) HTO flux on the surface | d)HTO washout coefficient |
| --- | --- | --- | --- |

Figure 5. Model’s outputs (, , ), for profiles № 4,5,6, as a function of rainfall rate (0.5, 3.0, 30 mm.h-1), for different temperatures: 00C (diamond), 150C (circle), and 300C (square).

| profile № 4 | profile № 5 | profile № 6 |
| --- | --- | --- |
| a) HTO concentration in the water in the air [g.ml-1] |
| b) HTO concentration in the rain water (g.ml-1) |
| c) HTO flux on the surface (g.s-2.s-1) - linear y axis |
| d) HTO flux on the surface (g.s-2.s-1) - logarithmic y axis |

Figure 6. Model’s outputs , , , for profiles №4,5,6; washout coefficient  is presented in (d) for all  distributions, for the three constant “profiles” № 1,2,3 and for profiles № 4,5,6.  Outputs are given for three different rainfall rates: 0.5 (diamond), 3.0 (circle), and 30 (square) mm.h-1;  temperature is 15 0C.

| a) HTO concentration in the water in the air | b) HTO concentration in the rain water | c) HTO flux on the surface | d) HTO washout coefficient |
| --- | --- | --- | --- |

Table 1. Typical variability of model's inputs

Symbol Inputs Units Range Typical

Numerical parameters

DRmin minimum raindrop size cm 0.000005 - 0.1 0.02

vertical grid step in the rain layer m 2 - 50 10

Cloud rain inputs

rain rate mm.h-1 0.5 - 30 3

downfall drop velocity m.s-1 between formulae (6) and (7) (6)

DSD drop size distribution cm-4 between formulae (10), (11), (12) (10)

Atmospheric inputs

temperature 0C 0 - 30 15

atmospheric pressure hPa 1000 - 500 950

HTO gaseous input

vertical profile of the HTO gas g cm-3 (distance from the souse ) 100 - 33000

Table 2.  Sensitivity in % of model’s outputs,,, to drop size distribution (Sekhorn-Srivastava - SS, Marshall-Palmer - MP and Best - B) for different rainfall rates (3, 0.5, 30 mm.h-1) and different downfall velocity formulae (Best, Kessler).  For details see the text.

,,

[mm.h-1] 3.0 0.5 30.0 3.0 0.5 30.0

of: Best Kessler Best Kessler Best Kessler Best Kessler Best Kessler Best Kessler

SS – MP 0.18 0.11 -12.0 -12.0 22.0 21.0 0.13 0.13 -15.0 -13.0 22.0 22.0

B – MP -52.0 -50.0 -48.0 -47.0 -52.0 -50.0 -44.0 -45.0 -46.0 -46.0 -46.0 -48.0

B – SS -52.0 -50.0 -37.0 -36.0 -72.0 -69.0 -44.0 -46.0 -32.0 -34.0 -66.0 -69.0

Table 3. Sensitivity in % of model’s outputs,,, to air temperature (00C or 150C), for different drop size distributions (MP, SS, B), rainfall rates (3, 0.5, 30 mm.h-1) and different downfall velocity formulae (Best, Kessler). For details see the text and equation (23).

,,

[mm.h-1] 3.0 0.5 30.0 3.0 0.5 30.0

of: Best Kessler Best Kessler Best Kessler Best Kessler Best Kessler Best Kessler

MP 49. 46. 62. 59. 32. 30. 38. 40. 53. 54. 23. 24.

SS 49. 46. 58. 55. 37. 35. 38. 40. 48. 49. 27. 29.

B 29. 27. 41. 39. 18. 17. 22. 23. 34. 35. 13. 14.