BRIEFING ON ACTUAL UNDERSTANDING ON TRITIUM WASHOUT

IFIN-HH (D. Galeriu, A. Melintescu), NIMH (D. Attanasov), CEA (L. Patryl, P. Guetat)

A report for International Atomic Energy Agency (IAEA) EMRAS II (Environmental Modelling for RAdiation Safety) Programme, Working Group 7 – “Tritium” Accidents, based on current results from various sources, including collaboration between IFIN-HH and National Institute of Meteorology and Hydrology, Sofia, Bulgaria and results from RFNC-VNIEF Sarov, Russia, also.

Tritiated water vapour from a nuclear power plant is continuously released to the atmosphere and then scavenged by precipitation. Rainout refers to in-cloud scavenging by precipitation of cloud droplets or ice crystals. Washout refers to below-cloud scavenging by precipitation.

The traditional goal of HTO washout studies is to determine the washout ratio:

=   						       [1]

and the washout coefficient :

Λ=    =  ,   (s-1) 				       [2]

where - the amount of HTO in a column with a bottom of unit area (g cm-2); J the flux of liquid HTO at the ground surface; Cf the mass concentration of the liquid HTO in the falling rain water; - the concentration of the vapour phase HTO in the drop's environment (g cm-3) at 1 m reference height.

For a given shape of the tritium-in-air vertical profile in a section of the plume, the rain concentrations are proportional to the vertical integral of tritium air concentration. In the case of gas scavenging, the factor of proportionality (x), otherwise called washout coefficient (rate), is not constant throughout the plume as in the case of aerosols, but depends on the shape of the vertical profile, and hence on the distance from the source.

As conclusions of the IAEA WG 7 EMRAS II Programme it was pointed out the needs that more efforts still have been done to decrease the uncertainty for tritium washout. In the actual programme EMRAS II, one of the working groups is WG 7 –“Tritium” Accidents and one of topic which must be clarified in this WG 7 is tritium washout. This note is a contribution to the topic.

The theory of washout of gaseous pollutants from the atmosphere was first comprehensively applied to tritiated water (HTO) vapour by Hales (1972 a, b) and his HTO washout concept has not changed substantially up to now. Experimental work was done for HTO in a limited number of conditions (Dana et al. 1978). Ogram (Ogram, 1985; Ogram et al., 1992) has reviewed precipitation scavenging model calculations for tritiated water vapour and key processes and input parameters for environmental tritium models.

In the absence of better information, it is recommended a washout coefficient with ( = 10-4 s-1 for light rain (~ 1 mm h-1) and ( = 10-3 s-1 for extremely heavy rainfall (~ 25 mm h-1) which may be used for calculations of HTO washout.

Experimental data of Dana et al. (1978) for a release at 60 m gives are given in Table 1.

Table 1. Experimental data (Dana et al., 1978) for a release at 60 m

| Rainfall Rate (mm.h-1) | Distance from release (m) | ( (s-1) |
| --- | --- | --- |
| 0.6 | 400 | 2.60 × 10-5 |
| 0.6 | 800 | 1.86 × 10-5 |

Tokuyama and Oonishi (1997) have reported 29 values monthly measured for the washout coefficient of HTO from Tsuruga area, Japan where there are 4 nuclear reactors. The mean value of the data has ( = (7.3 ± 4.1) × 10-5 s-1, with an average rainfall rate of 2 mm h-1.  Although the meteorological parameters, rainfall intensity, raindrop size, and raindrop size spectrum influence wet deposition by washout, only the monthly mean rainfall intensity data were available for the above study. On the opposite part of Japan, at Tokaimura, the yearly average of washout rate was ( = 4.6 x10-4 s-1, for the same precipitation intensity (Cf Pine scenario, EMRAS).

Yves Belot (Belot, 1998) attempted to assess the washout rate, using the Gaussian model in the frame of Hales theory (Hales, 1972b). Figure 1 presents the results for rain intensity of 1 mm h-1. Following this study (Belot, 1998), the washout coefficient can be considered proportional to rain intensity at power 0.7. The experimental results from Dana (Dana et al., 1978) are close with the model, but the high value in Tokaimura is out of model.

Figure 1. Washout coefficient of tritiated water in a plume originating from different release heights h; the rain intensity is 1 mm hr-1

Experimental work (Belavodsky et al., 1997) shows that “the concentration of HTO in the drop’s water is proportional to the concentration of HTO vapour, drop size and the drop’s duration of flight. Moreover, the average rate of exchange was 0.47±0.02 cm s-1”. The drop radii were: 0.14, 0.17 and 0.21 cm. The most probable rate limiting stage of the exchange mechanism is HTO convective diffusion through the concentration boundary layer of air when drops are falling.

Starting with an older revision of the topic (Ogram et al., 1992) an update on dry and wet deposition was done (Melintescu, 2002) and the need of improvement wet deposition modelling was emphasised. It was noticed that the Canadian Standard recommends a high value for the wet deposition, but a low value for plume depletion by rain.

Table 2. Canadian Standard recommendations for tritium washout (CAN 91

| Radionuclide / element | Washout coefficient, ( (s-1) |
| --- | --- |
|  | Rain intensity, mm h-1 | Snow intensity, mm h-1 |
|  | 0.5 | 1 | 3 | 5 | 0.5 | 1 | 3 | 5 |
| 3H and 131I |  |  |  |  |  |  |  |  |
| (I | 5×10-6 | 1×10-5 | 2×10-5 | 3×10-5 | <10-7 | 1×10-7 | 2×10-7 | 3×10-7 |
| (H | 1×10-4 | 2×10-4 | 4×10-4 | 6×10-4 | 2×10-7 | 4×10-7 | 8×10-7 | 1×10-6 |

The generalization of washout rate is:

(= a *(I/Io)b                                                               [3]

The German standard (MFG-90) recommends for tritium b=1 and a= 3.5x10-5.

Some compiled values since 2002 are given in Table 3:

Table 3. Compiled values since 2002 for tritium washout (Melintescu, 2002)

| Reference | ( (s-1), at 1 mm/h | exponent b or rain intensity |
| --- | --- | --- |
| German Standard | 3.5 10-5 | b= 1. |
| Canadian Standard | 1.8 × 10-4 | b= 0.73 |
| Dana et al, 1978 | [1.8-2.6] × 10-5 | I=0.6 mm h-1 |
| Tokuyama and Oonishi, 1997 | (7.3±4.1) × 10-5 | I =2 mm h-1 |
| Ogram, 1995 | 1 × 10-4 (10°C) | b=0.77 |
| Belot, 1998 | 6 10-5 | b= 0.7 |

The recommended values in 2002 were:

A = 6x10-5  s-1  ;    b=0.73

The large uncertainty in the assessment of tritium washout comes also from the paucity of experimental data. Between 1999 and 2002 experiments have been done in VNIEF (Sarov, Rusia under the ISTC Project 654) considering emissions from 30 m height and observation of rain concentration at a radius of 150 m (Golubev et al., 2002 a - d, 2003).

Washout rate ( has been estimated using experimental results in a following way:

[4]

where:

- is the wind velocity, m s-1;

- is the precipitation intensity, m s-1;

- is the HTO source intensity, Bq s-1;

- is the tritium concentration in rainwater in the i-th sampler, Bq m-3;

- is the arc length between the i-th and the i+1-th sampler, m.

During the experiments, the air temperature, wind speed and its direction and rain intensity were recorded. The wind velocity for each of the experiments was taken as an average value. Rain intensity in all the experiments was assumed to be about 1 mm h-1. The release rate was estimated an average value during the entire experiment.

The following two models were developed and validated: simple engineering model and complex exchange kinetics model, respectively. Figure 2 represents observed and modelling results for engineering model and the vapour / raindrop exchange model, respectively. It can be seen that the “drop” model describes the experimental data “from the top” and simple model – those “from the bottom”. The engineering models consider the washout ratio (rain concentration (Bq L-1) over air moisture concentration (Bq L-1)) and give a ratio near 0.4. The process model (top down) uses the Gaussian HTO profile and gives a washout rate of ~14.5x10-5 s-1, for a rain intensity of 1 mm h-1. This is 2 times more than the previous predictions (Belot, 1998) and relatively closes to Ogram assessment (Ogram, 1985). In order to explain the prediction difference we will refer to some specific results.

Figure 2. Comparison of experimental results with modeling results due to the Gauss model and the model with the drop

The recent experiments emphasize also the high variability of rain intensity (Figure 3) and the variability of rain drop diameter distribution (Figure 4) at various rain intensities. The model used by VNIEF Sarov considers the effect of wind velocity on falling drop together with the net effect of an increased drop trajectory. Figure 5 gives the concentration in air and drop, along the trajectories for a small drop and a large one.

Figure 3. Dependence of rain with time (each of the points is the result of averaging over the 1-min duration interval)

Figure 4.  Size distribution N(D) (m-3mm-1)  vs. diameter V(D) and for raindrops within interval 7 and 1 (duration 1 min).

Figure 5 Distribution of HTO concentrations in the drop and atmosphere along the trajectory of the drop falling.

Comparison of the simplest washout model – Сrain=((Catm with the experimental data have shown that the value (=0.4 allows description of averaged experimental data in the best way. At the same time, the values of (  coefficient are as following: for the wind velocities of ~ 3 m s-1 is 0.35, and for wind velocities of ~ 6 m s-1 is 0.45.  The process oriented level model developed by VNIEF (Sarov) accurately describes experimental results and gives higher values for washout coefficient in the vicinity of the source or  far away from the source. The explicit introduction of wind velocity and a better choice of drop velocity formula explain the difference versus Belot model (Belot, 1998).

In parallel with VNIEF research, Hales (Hales 2002) published an update of his model. The approach takes the form of a set of analytical equations that correspond to 5 types of Gaussian plume formulations: standard bivariate-normal point-source plumes, line-source plumes, unrestricted instantaneous puffs, and point-source plumes and puffs that experience reflection from inversion layers aloft. These equations represent the concentration of scavenged pollutants in falling raindrops and are similar in complexity to their associated gas-phase plume equations. They are strictly linear, thus allowing superposition of wet-deposition contributions by multiple plumes. Numerical solution and analytical approximation are given but up to now; there is no direct application for tritium (HTO).

The above approaches use the Gaussian approximation for the air concentration and selected empirical formulae for the rain drip distributions and drop falling velocity. An attempt to generalize the washout modelling was done recently (Atanassov and Galeriu, 2009), in the frame of a collaboration between IFIN-HH and Bulgarian Meteorology researchers. A numerical Eulerian model that describes washout independently of dispersion is developed. The model is developed to be used as a subroutine in tritium specific models interfaced with any sophisticated dispersion model.

Different size distributions of raindrops and different formulae for drop downfall velocity are considered.  A sensitivity analysis to these and other model parameters is performed. Recommendations for some numerical techniques are made. Three empirical formulae for drop size distribution and two for downfall drop velocity were used. The sensitivity analysis has shown that the washout process is influenced most significantly by rainfall parameters and air temperature: different raindrop size distributions cause differences of up to about 70 % in the washout outputs; a change of 15 0C in the air temperature causes an effect of about 50 %. Unlike temperature, which is usually well known, rainfall parameters are difficult to be precisely established, that can lead to substantially wrong washout estimates. The general conclusion is that the washout process is too complex to be comprehensively described by the simple washout coefficient concept. The approach proposed here for directly calculating the outputs like concentration and flux is preferable; anyway the washout coefficient is needed mostly for the assessment of these outputs. The largest potential for improvements in tritium washout modelling is related to comprehensive input information for cloud and rain processes that becomes easily available today. The paper distinguishes between absolute outputs, as liquid HTO concentration in the rainfall, and the downward flux of liquid HTO, in contradiction with relative outputs, as the washout ratio and washout coefficient. The washout ratio and washout coefficient are characteristics of the washout process that are needed to calculate the absolute outputs.

An example of results is given in Figure 6 for the case of a HTO profile in the air and 2 temperatures. The influence of temperature and drop diameter is emphasized.

Figure 6. Changes of HTO concentration in drops of different diameter (0.02, 0.075, 0.25 cm) during their downfall, for the HTO profile (left of figure) and for constant over  temperatures of 15 0C and 0 0C.  Rainfall rate is 3 mm h-1.

In the case of a rain intensity of 2 mm h-1 and a constant HTO concentration in air up to 500 m height, the washout coefficient as function of temperature is given in Figure 7.

Figure 7. The washout coefficient of HTO for a rain intensity of 2 mm h-1

The main contribution of this recent paper is the giving up to the constraints of the Gaussian approach, emphasizing the role of rain drop distribution. Major nuclear units with large tritium loads are generally situated in complex terrains and the Gaussian plume is a crude estimate of air concentration profile. Also various type of rain (as classified by World meteorological Organisation) have distinct rain drop distribution.

Combining these recent approaches with the influence of wind velocity on the drop trajectory, it can give a solution to decrease the uncertainty. Wind and temperature profile can be now obtained form remote sensing, but the rain drop distribution remains the main problem.

HTO WET DEPOSITION IN WINTER

The dose impact of tritium released to the atmosphere in winter is far from being understood.  Some experimental data on dry and wet deposition were obtained in the past (Papadopoulos et al. 1986; Davis, 1997), but little experimental information is available on the persistence of tritiated water in the snow pack. The dry deposition velocity (v,) of HTO to snow was found to be I.6 x 10-3 ( 0.5 x 10-3 m s-l; the washout coefficient of HTO by snow was 2.1 x l0-5 ( 1.0 x l0-5 s-1. Some authors (Konig et al., 1984) report a semi-empirical value of 2.6 x 10-5 s-1 for a snowfall rate of 1 mm h-1 water equivalent.

The Canadian standard (CAN 91) recommends a range between minim and maxim values and these recommendations are lower then experimental values for the snow washout (Table 2).

It seems clear that old recommendation were grossly underestimated. More experiments are still needed.

The diffusion and persistence of HTO in the snow pack was also observed (Galeriu et al., 2009). In conditions of cold weather and dry snow, the diffusion coefficient lies in the range of 1 ÷ 2 x 10-10 m2 s-1; it is an order of magnitude lower than diffusion in water, but an order of magnitude higher than self-diffusion in ice. In spring, when the snow melts, about 70 % from the initial fallout remains.

HTO DEPOSITION BY FOG

We do not find any experimental results on HTO deposition in foggy conditions. We will try to make some general considerations.

The properties of radiation or coastal fog are given below (Justio, 1981).

Table 5. Characteristics of fog

Measurements for a radiation fog with natural aerosols of Ca (median diameter near 2 () show a deposition velocity of 10-2 m s-1, for a fog flux of 0.5-15 g m-2 h-1 (EC95). A preliminary assessment for deposition in fog conditions has been reported (Gibb et al., 1998) using data for chemical pollution.

Minimum and maximum deposition velocities are recommended as function of fog flux.

Table 6. Deposition velocity in fog

| Fog flux (mm h-1) | 0.01 | 0.05 | 0.10 | 0.50 | 1.00 | 2.00 |
| --- | --- | --- | --- | --- | --- | --- |
| Vd (low) cm s-1 | 1 | 3 | 7 | 35 | 70 | 140 |
| Vd (high) cm s-1 | 3 | 14 | 28 | 140 | 280 | 560 |

Typical fog fluxes are also given in Table 7.

Table 7. Fog flux on typical surfaces

| Fluxes | soil | Snow | water | grass | closed forest | forest edge |
| --- | --- | --- | --- | --- | --- | --- |
| Flow (mm h-1) | 0.01 | 0.01 | 0.01 | 0.01 | 0.1 | 0.5 |
| Fhigh (mm h-1) | 0.05 | 0.05 | 0.1 | 0.1 | 0.5 | 2. |

For cultivated land we expect a fog flux near 0.05 mm h-1. In order to estimate the HTO deposition we use the dependency of drop HTO concentration on drop radius (Golubev et al., 2003) and it is given in Figure 8.

Figure 8. Ratio dependence of the HTO concentration in the drop (and in the moisture condensed from the atmosphere at 1 m height from the surface) on the drop diameter

In Figure 8 it is seen that the concentration in fog droplet is very close with air moisture and deposition in fog conditions is 2-3 times higher than in rain conditions of the same intensity.

References

Hales J. M. 1972a Scavenging of Gaseous Tritium Compounds by Rain, BNWL-1659, Battelle, Pacific Northwest Laboratories, Richland, Washington.

Hales J. M. 1972b Fundamentals of the theory of gas scavenging by rain. Atmospheric  Environment. 6, 635-659.

Dana M.T., Wogman N.A. and Wolf M.A., 1978, Rain scavenging of tritiated water (HTO). A field experiment and theoretical considerations.  Atmospheric  Environment. 12, 1523-1529.

Ogram G.L., 1985, Precipitation scavenging of tritiated water vapour (HTO), Report 85-233-K, Ontario hydro research division.

Ogram G.L., Bunnenberg C., and Taschner M., 1992, Key processes and Input Parameters for Environmental Tritium Models, CFFTP Report Net-Contract-No. 88-176, May 1992.

Tokuyama H. and Oonishi M. Precipitation washout of tritiated water vapor from a nuclear reactor Journal of Environmental Radioactivity. Volume 34, Issue 1, 1997, Pages 59-68

Belot Y., Predicting the washout of tritiated water from the atmospheric plumes, Workshop of the IAEA Task Group on Tritium Safety and Environmental Effect, AECL, Chalk River, Canada, 1998

Belovodsky L.F, Gaevoy V.K, Golubev A.V. et al, Tritium oxide wash-out by drops, J. Environ. Radioactivity, 36, 2-3, 129 (1997).

Melintescu A, 2002, Processes and parameters in modeling dry and wet deposition of radionuclides (in Romanian), part of PhD thesis

A.V.Golubev, A.Y. Aleinikov, V.N.Golubeva, M.M. Khabibulin, M.V.Glagolev,

S.E.Misatyuk, S.V. Mavrin Studies of HT and HTO behavior in the vicinity of long-term emission source: Model – experiment intercomparison WM’03 Conference, February 23-27, 2003, Tucson, AZ

Golubev A., Khabibulin M., Mavrin S. (2002a). Studies of HTO washout and deposition in the vicinity of emission source. Radioprotection  Vol. 37, C1 (2002), pp

Golubev A., Glagolev M., Misatuk S. Studies of HTO transport and oxidation in unsaturated soil. Radioprotection, v.37, C1 (2002b). p. C1-237-241

Golubev A.V., Aleinicov A.Y., Golubeva V.N. et al.  Studies of HTO washout and deposition in the vicinity of emission sourcel II: model-experiment intercompararision. // Fusion Science and Technology. 2002c. Vol. 41, №3, p. 474-477.

A.V. Golubev, project manager RESEARCHES INTO THE ENVIRONMENTAL TRITIUM MODEL BEHAVIOR, Final report under ISTC project 654-99,, RFNC-VNIIEF, Sarov 2002d

Hales J. M. 2002 Wet Removal of Pollutants from gaussian Plumes: basic Linear Equations and Computational Approaches.  J. Appl. Met., vol.41, 905-918

## D. Atanassov, D. Galeriu 2009, Rain Scavenging of Tritiated Water Vapour: A Numerical Eulerian Stationary Model, submitted to Atm. Envir

Papadopoulos, D., Konis, L.A., Langguth, K.G. and Fark, S. (1986).  Contamination of

precipitation due to tritium release into the atmosphere.  Radiat. Prot. Dosim. 16:95-100.

Davis, P.A., Cornett, R.J., Killey, R.W.D., Wood, M.J. and Workman, W.J.G. (1992).

Environmental behaviour of tritium released to the atmosphere in winter.  Fusion Technol.

21: 651-658.

CAN-91.  CAN/CSA-N288.2-M91, Table 6.2, p.46 ‘Guidelines for Calculating Radiation Doses to the Public from a Release of  Airborne Radioactive Material under Hypothetical Accident Conditions in Nuclear Reactors’, 1991.

Justio, J E (1981). Fog Structure. In Clouds: their Formation, Optical Properties and Effects. ed HOBBS, P V and DEEPAK, A, Academic Press.

[Gibb 1998] R Gibb, P Carson, W Thompson The effect of fog on radionuclide deposition velocities. Canadian Nuclear Association, Annual Meeting 1998

[EC95]   European Commission - Radiation Protection- Deposition of radionuclides, their subsequent relocation in the environment and resulting implications  Final Report  EUR 16604, Luxemburg 1995

MFG-90, German Federal Monitor nr 64a, 31 March 1990

Davis, P.A. (1997).  Tritium transfer parameters for the winter environment. .J. Environ. Radioactivity, Vol. 36, No. 2~.3, pp. 177-196, 1997

# Comments

Must be checked

Reference to be add